## Slide 1: Community Hydrological Modelling Workflows
Online Training Session with Federal, Provincial, and Territorial Partners
Kasra Keshavarz
Research Scientist
Schulich School of Engineering
University of Calgary
March 21st, 2024
Alain Piteroniro, PhD, PEng
Professor and Canada Research Chair
Schulich School of Engineering
University of Calgary

## Slide 2: Acknowledgements
Special thanks to:
Wouter Knoben (Ucalgary), Shervan Gharari (Usask), Martyn Clark (Ucalgary), Ala Bahrami (Usask), Guoqiang Tang (NCAR), Cooper Albano (Usask) , John Pomeroy (Usask), Dan Princz (ECCC), Travis Logan (Ouranos), Pierre Pellerin (Ouranos), Dikraa Khedhaouiria (ECCC) and everyone present today in the session
Notes: Federal OK?
MESH model is being done like right now, so it is important.
Side buttons could be skipped (only explaining the necessities)

## Slide 3: Outline
Community Hydrological Modelling Recipe
Digital Infrastructure on Digital Research Alliance of Canada’s HPCs
Introducing Community Workflows & Tools
Practice Example – Bow River At Banff
Troubleshooting

## Slide 4: Outline
Community Hydrological Modelling Recipe
Digital Infrastructure on Digital Research Alliance of Canada’s HPCs
Introducing Community Workflows & Tools
Practice Example – Bow River At Banff
Troubleshooting

## Slide 5: Recipe for Community Hydrological Modelling
Knoben, W. J. M., Clark, M. P., Bales, J., Bennett, A., Gharari, S., Marsh, C. B., Nijssen, B., Pietroniro, A., Spiteri, R. J., Tang, G., Tarboton D. G. & Wood, A. W. (2022). Community Workflows to Advance Reproducibility in Hydrologic Modeling: Separating Model‐Agnostic and Model‐Specific Configuration Steps in Applications of Large‐Domain Hydrologic Models. Water Resources Research, 58(11), e2021WR031753.
Developing relevant workflows on High Performance Computing (HPC) facilities
Keeping workflows open source and reproducible for the scientific community
Keeping workflows efficient for real-world applications
Separate “model-agnostic” and “model-specific” configuration parts

## Slide 6: Outline
Community Hydrological Modelling Recipe
Digital Infrastructure on Digital Research Alliance of Canada’s HPCs
Introducing Community Workflows & Tools
Practice Example – Bow River At Banff
Troubleshooting

## Slide 7: Digital Infrastructure
Graham
@ UWaterloo
Science and Policy
Decisions
Subset
Regrid
Visualize
Temporal Disaggregate
HPC
Tailored
Remap
Suite of tools to facilitate hydrological modelling and data processing:
Generalizing approaches applicable to data processing applications
Using stable tools to assure robust performance on HPC platforms
Credit: Dr. Shervan Gharari

## Slide 8: Digital Infrastructure
Remote access
accounts
rpp-kshook
rrg-mclark
Graham
@ UWaterloo

## Slide 9: Digital Infrastructure
Our recommendation is to access Graham using either of the following methods:
Terminal
Multi-user environment
Resource efficient
Collaborative environment
Reproducibility mechanisms
Strong community support
Ease of use
Maximal flexibility
Remote Access
Steep learning curve
Full control of command sessions
Strong community support
https://jupyterhub.sharcnet.ca/
$ ssh USERNAME@graham.alliancecan.ca
MobaXTerm
PuTTY
MacOS Terminal
Notes: JupyterHub: https://jupyterhub.sharcnet.ca/

## Slide 10
Any questions so far?

## Slide 11: Digital Infrastructure
DALLE generated image
High Performance Computing (HPC) systems are comprised of various “nodes”
The idea is to expand horizontally, instead of vertically.
HPC “nodes” are located inside a
“rack enclosure”
JupyterHub server lands your JupyterLab session on one these nodes
or, more clearly, “computing” nodes
On Digital Research Alliance HPCs, computing nodes do not have access to an active internet connection unfortunately

## Slide 12: Digital Infrastructure
Multi-user Server Service for Jupyter Sessions
User Authentication Capability
Resource Customization
Customizable Work Environment
Alliance Canada username
*********
https://jupyterhub.sharcnet.ca/
Notes: JupyterHub: https://jupyterhub.sharcnet.ca/

## Slide 13: Digital Infrastructure
Safe to ignore
rpp-kshook
rrg-mclark
How many cores you need?
4 is more than enough for today
Today’s session is
3 hours only
How much memory you need?
16000 MB is enough for today
Do we do any Deep Learning?
No.
Strong recommendation is to use
JupyterLab interface
Notes: JupyterHub: https://jupyterhub.sharcnet.ca/

## Slide 14: Digital Infrastructure
https://jupyterhub.sharcnet.ca/
General tips:
Understand your setup: Be resourceful! Asking too much computational resource can keep you in the queue forever; public HPCs are shared resources. Asking for too little resources can make your Jupyter session slow and laggy.
Choose the Right Kernel: Be mindful! Jupyter provides you with all sort of programming environments; make sure to choose the right (customized) programming kernel for your work.
Monitor Performance and Document: Be diligent! As you work more with the environment, you get to know the requirements of your computations. Keep track of your workflow’s performance and document your work.
DALLE generated image
DALLE generated image
Notes: JupyterHub: https://jupyterhub.sharcnet.ca/

## Slide 15: Digital Infrastructure
Simple file browser
List of running kernels
GPU list (is your workflow for Deep Learning?)
Headers of your notebooks (just like your physical notebooks)
List of HPC modules
(explained later)
Jupyter Extensions
(disabled)
Kernel Status
List of kernels
as Notebooks
List of kernels
as consoles
Useful tools
Manu bar
Debug tools

## Slide 16: Digital Infrastructure
HPCs comes with various
“modules”
Different users have different requirements
Flexibility
Users may need specific versions of software or libraries
Customization
Optimization
software packages are often optimized for the underlying hardware architecture
Having commonly used software readily available saves users time and effort
Productivity
But where are they?
DALLE generated image

## Slide 17: Digital Infrastructure
List of HPC modules
(LMOD Extention)
Loaded modules
Unloaded modules
A saved list of modules
is called a “collection”
Create a collection
out of loaded modules
Restore a previously
saved collection
Using JupyterLab interface
For creating collections could be time consuming.
We will use the Terminal to build a collection later.

## Slide 18: Digital Infrastructure
username
Computing node name
Current working directory
tilda means home
All instructions are available on this presentation's repository:
https://github.com/kasra-keshavarz/community-modelling-workflow-training

## Slide 19: Digital Infrastructure
username
Computing node name
Current working directory
tilda means home
All instructions are available on this presentation's repository:
https://github.com/kasra-keshavarz/community-modelling-workflow-training
Loading
“Standard Environment”
Loading
Gnu C Compiler
version 9.3.0
Loading
every module we need
Saving all modules as
a “collection” called
“science modules”
Exactly similar to what
we can do in this tab
Notes: https://github.com/kasra-keshavarz/community-modelling-workflow-training

## Slide 20: Digital Infrastructure
Refresh the JupyterLab session webpage, and see if you can find the collection you just saved:
Check out what module
collections you have
Restore the “scimods”
(science modules)
Wait for a few seconds
so Jupyter loads all
modules saved in
“scimods” collection
This is only a one-time process. You can always access all the collections you saved from Jupyter’s LMOD Extention tab

## Slide 21
Any questions so far?

## Slide 22: Digital Infrastructure
Python Programming Language
Community Hydrological Modelling Workflows: much of our workflows are offered in Python package formats
Python is Powerful: Python always can offer you a useful workflow
Reproducible Environments: Python’s Virtual Environments enables this requirement
Supported on HPCs and Commercial Cloud regardless of your Operating System: it can be used everywhere
Graham is no exception: Python is fully supported on Graham
Notes: We need to download the repository too

## Slide 23: Digital Infrastructure
Before setting up the Python Environment, we
need to download the training session’s GitHub repository

## Slide 24: Digital Infrastructure
DALLE generated image
High Performance Computing (HPC) systems are comprised of various “nodes”
The idea is to expand horizontally, instead of vertically.
HPC “nodes” are located inside a
“rack enclosure”
JupyterHub server lands your JupyterLab session on one these nodes
or, more clearly, “computing” nodes
On Digital Research Alliance HPCs, computing nodes do not have access to an active internet connection unfortunately

## Slide 25: Digital Infrastructure
First, we need to switch to the “login node”
Login nodes do have access to an active internet connection
Secure SHell (ssh) to a login node of choice
Enter your Digital Research Alliance account password
Notes: More information on nodes: https://docs.alliancecan.ca/wiki/Graham

## Slide 26: Digital Infrastructure
We use this terminal session now to download the relevant GitHub repository
You are logged into a “login node” with an active internet connection

## Slide 27: Digital Infrastructure
Create a “github-repos” directory to organize downloaded repositories
“clone”-ing the repository

## Slide 28: Digital Infrastructure
1 | Only for personal use | Home space 50 GB per user
2 | Only for data processing | Scratch space 20 TB per user
3 | NOT for personal use – only for shared resources | Project space rrp-kshook: 2.5 PB rrg-mclark: 0.2 PB

## Slide 29
Any questions so far?

## Slide 30: Digital Infrastructure
Let’s set up our Python virtual environment
DALLE generated image

## Slide 31: Digital Infrastructure
Although the modules are loaded in your JupyterLab session, Terminal is a separate entity, and we must reload the modules there as well:
restoring
“scimods”
Checking what
has been loaded
Is it equal to the
list on left?

## Slide 32: Digital Infrastructure
Are we all using the same version?

## Slide 33: Digital Infrastructure
Now build a Python
Virtual Environment;
put it under the
“virtual-envs” directory,
and call it “scienv” after
switching to a “login node”
“virtual-envs” directory
is in your home directory

## Slide 34: Digital Infrastructure
After creation, let’s activate the virtual environment
Install the packages included in the training session’s repository
Notes: Switching to login need is mandatory

## Slide 35: Digital Infrastructure
“scienv” virtual environment is now accessible through JupyterLab

## Slide 36: Digital Infrastructure
The “scienv” (science
environment) kernel is
now recognized by
Jupyter
Refresh the JupyterLab session webpage, and see if you can find the collection you just saved:

## Slide 37: Outline
Community Hydrological Modelling Recipe
Digital Infrastructure on Digital Research Alliance of Canada’s HPCs
Introducing Community Workflows & Tools
Practice Example – Bow River At Banff
Troubleshooting

## Slide 38: Introducing Community Workflows & Tools
Command Line Interface
(CLI)
NCAR-GWF WRF CONUS I
ECMWF ERA5
ECCC RDRSv2.1
NCAR-GWF WRF CONUS II
CCRN CanRCM4-WFDEI-CaPA
https://github.com/kasra-keshavarz/datatool
Steps:
1. Login to Digital Alliance of Canada (formerly Compute Canada) Graham cluster,
2. Make sure you have access to the designated project space and allocation,
3. Clone the remote GitHub repository,
4. Subset any spatial and temporal extents of interest for any of the available datasets
with only one line of code.
CCRN WFDEI-GEM-CaPA
.
.
.
~1 PB of data
(and growing)
AMES GDDP-CMIP6
Ouranos ESPO-G6-R2 RDRSv2.1
Ouranos CRCM5-CMPI6
DALL-E generate image
Notes: https://github.com/kasra-keshavarz/datatool

## Slide 39: Introducing Community Workflows & Tools
Command Line Interface
(CLI)
MERIT-Hydro
Soil Grids V1
MODIS Land Cover
https://github.com/kasra-keshavarz/gistool
Steps:
1. Login to Digital Alliance of Canada (formerly Compute Canada) Graham cluster,
2. Make sure you have access to the designated project space and allocation,
3. Clone the repository,
4. Subset and/or implement zonal statistics for any spatial and temporal extents of interest
for any of the included datasets with only one line of code.
Subsetting Geo-spatial data in GeoTIFF format
Implementing Zonal Statistics for ESRI Shapefiles efficiently
Calculating Slope & Aspect [in progress]
HRUs discretization in any spatial scale [in progress]
Landsat NALCMS
Depth to bedrock
Global Soil Dataset (GSDE)
.
.
.

## Slide 40: Introducing Community Workflows & Tools
https://github.com/ShervanGharari/EASYMORE.git
Command Line Interface (CLI)
and
Python Library

## Slide 41
Any questions so far?

## Slide 42: Outline
Community Hydrological Modelling Recipe
Digital Infrastructure on Digital Research Alliance of Canada’s HPCs
Introducing Community Workflows & Tools
Practice Example – Bow River At Banff
Troubleshooting

## Slide 43: Practice Example – Bow River at Banff
All instructions are available on this presentation's repository:
https://github.com/kasra-keshavarz/community-modelling-workflow-training
Bow River at Banff
Sub-basins and river network extracted from MERIT-Basins using Hydrant v0.1.0-dev0
Banff

## Slide 44: Practice Example – Bow River at Banff
First step is to extract a geospatial fabric
for the area of interest
DALLE generated image

## Slide 45: Practice Example – Bow River at Banff
What information is provided through MERIT-Basins?
25 km2 drainage area threshold for channels
Corrected/refined basin/region definitions
Below 25 km2 non-channelized areas along the coast or some endorheic areas (incomplete catchments or hillslopes) excluded
~2.94 million river reaches (unit catchments)
River network:
River segment IDs (COMID)
Downstream segment IDs (NextDownID)
Slope (slope)
Length (lengthkm)
Upstream segment IDs (up1-4)
Upstream drainage area (uparea)
River geometries
MERIT-Basins webpage: https://www.reachhydro.org/home/params/merit-basins
Subbasins:
Identical subbasin IDs (COMID)
Subbasin area (unitarea)
Subbasin geometries
Non-contributing areas:
Non-contributing area IDs (FID)
Non-contributing area geometries

## Slide 46: Practice Example – Bow River at Banff
Bow River at Banff
Sub-basins and river network extracted from MERIT-Basins using Hydrant v0.1.0-dev0
What typical information we usually need from a hydrography dataset for vector-based hydrological modelling?
River network:
River segment ID values
Immediate downstream segment ID values
Length Depending on your routing scheme you may need:
Slope [optional]
Width [optional]
etc.
Good read: http://switchfromshapefile.org
Subbasins:
Subbasin ID values
Correspondence Mapping Table between Subbasin and River Segment IDs (could be identical value)
Subbasin Area [optional]
etc.

## Slide 47: Practice Example – Bow River at Banff
Bow River at Banff
Sub-basins and river network extracted from MERIT-Basins using Hydrant v0.1.0-dev0
How does HydrAnT help us?
Hydrant’s documentation: https://hydrantpy.readthedocs.org
Extracting subsets of hydrography datasets given a point or a boundary area,
Hydrant is data-agnostic; if the input hydrography is valid and standard, you can use Hydrant,
Common sanity checks for datasets:
  Is water going upstream?
  Is there a cycle of river segments?
  etc.
Aggregation methods to dissolve elements of hydrography datasets
Knowledge extraction:
  What is the longest branch of river segments?
  What are the upstream segment of a certain point in the river network?
  What are the downstream segments of a river segment?
  What are the Strahler order of river segment?

## Slide 48
Any questions so far?

## Slide 49: Practice Example – Bow River at Banff
Navigate using JupyterLab file browser

## Slide 50: Practice Example – Bow River at Banff
Navigate using JupyterLab file browser

## Slide 51: Practice Example – Bow River at Banff
Use “Shift + Enter” to execute Notebook cells
Notebook cells
Double click to launch the Notebook
Tip: review keyboard shortcuts!

## Slide 52: Practice Example – Bow River at Banff
Switching to the relevant Jupyter Notebook
webpage

## Slide 53: Practice Example – Bow River at Banff
You can view the extracted geospatial fabric in a typical GIS program, such as QGIS

## Slide 54: Practice Example – Bow River at Banff
Second step is to run the model-agnostic
processes
DALLE generated image

## Slide 55: Practice Example – Bow River at Banff
Through a tool called “agnostic orchestrator” all the relevant data needed for this setup is processed by the Graham HPC
We have previously downloaded all the relevant tools for the “agnostic” step
We use the “agnostic orchestrator” configuration file instruct the file processing hierarchy

## Slide 56: Practice Example – Bow River at Banff
Agnostic workflow execution using its
“Orchestrator”
Editing “agnostic” configuration step

## Slide 57: Practice Example – Bow River at Banff
Executable paths
Executable arguments and options
(empty options are not provided to the script)
This is the only file for the “agnostic” step
Orchestrator configuration file

## Slide 58: Practice Example – Bow River at Banff
Geospatial data zonal statistics
NetCDF Aerial Averaging
#1
#2
#4
#3
#
: Order of process
Automated and ordered job
submission to HPC
NetCDF subset
-1: no order
ordered integers: order of processes

## Slide 59: Practice Example – Bow River at Banff
Switching to the JupyterLab webpage
for a quick overview
Execute the “agnostic orchestrator” in the Terminal using:
$ ./model-agnostic.sh model-agnostic.json

## Slide 60
Any questions so far?

## Slide 61: Practice Example – Bow River at Banff
Third and final step is to run the model-specific
processes
DALLE generated image

## Slide 62: Practice Example – Bow River at Banff
The specific part is written into a Jupyter Notebook
(it can be written as a script or any other form that you prefer)
Meshflow is the package to build a MESH model out of all the data we processed so far
The root address of where the data is stored

## Slide 63: Practice Example – Bow River at Banff
River network geometry file
Subbasin geometry file
Landcover fractions file(s)
Prepared forcing file(s)
List of variables to be used
Variables’ default units in the NetCDF files
Units of variables that MESH requires

## Slide 64: Practice Example – Bow River at Banff
River Segment/Subbasin ID
Downstream river segment/subbasin ID
Landcover classes of the landcover dataset used
All the variables to be used in the “drainage database” MESH file
Units of variables to be included in the “drainage database” MESH file

## Slide 65: Practice Example – Bow River at Banff
Units of variables in the “drainage database” file that MESH requires
Minimum values of “drainage database” MESH file
Renaming GRU dimension name in the MESH “drainage database” file to satisfy diverse versions of MESH
Renaming sub-basin dimension name in the MESH “drainage database” file if needed
The value of the outlet river segments created using “Hydrant”
(Hydrant default is -9999)
Initiate an instance of the MESHWorkflow object
And running the “model-specific” step

## Slide 66: Practice Example – Bow River at Banff
Switching to the JupyterLab webpage
for a quick overview

## Slide 67
Any questions so far?

## Slide 68: Outline
Community Hydrological Modelling Recipe
Digital Infrastructure on Digital Research Alliance of Canada’s HPCs
Setting Up Your Account on HPCs
Introducing Community Workflows & Tools
Practice Example – Bow River At Banff
Troubleshooting

## Slide 69: Troubleshooting
Whenever you face an issue, follow the steps below:
“Agnostic” log files are located in the following directories:
$HOME/.datatool
$HOME/.gistool
/path/to/EASYMORE/s/temp/directory
/path/to/agnostic/orchestrator/s/directory
  Look for files with the following extensions:
.out, .err, .log
  Try to understand what has gone wrong. In 80% of the time, there is a minor human error involved.

## Slide 70: Troubleshooting
Continuing…
Make sure Graham storages are responsive, very often than not, the home, scratch, or project spaces experience technical difficulties
Make sure you have enough space on any storage you are working; the quota command can show you how much storage you are using
If the project space gets full, communicate this with your PI; users do mistakenly fill up the shared storage without much justification,
Try troubleshooting technical issues using ChatGPT or any online ChatBot you have access to

## Slide 71: Troubleshooting
Try troubleshooting by Google-ing and searching Stackoverflow
Avoid using chat mechanisms to exchange critical information; everything needs to be documented properly; undocumented work equals to null
If nothing worked out, open an “Issue” on the relevant GitHub repository(-ies) providing an MCVE
Feel free to contribute to any repository you are interested in. Whenever you commit, follow the commit guidelines recommended by the creator of Git
Fix MESH bugs
Notes: minimal complete verifiable example

## Slide 72: Troubleshooting
Linus Torvalds – creator of Linux and Git
Same philosophy applies to GitHub Issues

## Slide 73: Thank you for attending
https://ucalgary.ca/civil