## Slide 1: Community Hydrological Modelling Workflows
Online Training Session with Federal, Provincial, Territorial, and International Partners
Kasra Keshavarz
Research Scientist
Schulich School of Engineering
University of Calgary
February 18th, 2025
Alain Pietroniro, PhD, PEng
Professor and Canada Research Chair
Schulich School of Engineering
University of Calgary
Martyn Clark, PhD
Professor and Schulich Research Chair
United Nations Hub Co-Director
Schulich School of Engineering
University of Calgary
Darri Eythorsson, PhD
Postdoctoral Associate
Schulich School of Engineering
University of Calgary

## Slide 2: Acknowledgements
Notes: Federal OK?
MESH model is being done like right now, so it is important.
Side buttons could be skipped (only explaining the necessities)

## Slide 3: Outline
Community Hydrological Modelling Recipes
Computational Resources for the Training Session
Setting up ECCC’s National Water Model—MESH
Introduction and Preview of CONFLUENCE

## Slide 4: Outline
Community Hydrological Modelling Recipes
Computational Resources for the Training Session
Setting up ECCC’s National Water Model—MESH
Introduction and Preview of CONFLUENCE

## Slide 5: Recipe for Community Hydrological Modelling
Knoben, W. J. M., Clark, M. P., Bales, J., Bennett, A., Gharari, S., Marsh, C. B., Nijssen, B., Pietroniro, A., Spiteri, R. J., Tang, G., Tarboton D. G. & Wood, A. W. (2022). Community Workflows to Advance Reproducibility in Hydrologic Modeling: Separating Model‐Agnostic and Model‐Specific Configuration Steps in Applications of Large‐Domain Hydrologic Models. Water Resources Research, 58(11), e2021WR031753.
Community Workflows to Advance Reproducibility in Hydrologic Modeling (CWARHM)
Developing first generation of community hydrological modelling workflows
Keeping workflows open source and reproducible
Keeping workflows efficient for real-world applications
Separating model-agnostic and model-specific configuration parts

## Slide 6: Recipe for Community Hydrological Modelling
Submitted to Water Resources Research, under review
Enhancing and proposing model-agnostic and model-specific engines for HPC environments
Modularized methodology for the model-agnostic step for various data types and preprocessing needs
Expanding model-specific workflows for other community modelling systems including ECCC MESH and SMHI HYPE
Proposing strategies to objectively orchestrate the configuration stage of hydrological models

## Slide 7: Recipe for Community Hydrological Modelling
Extended workflow to seamlessly include:
•Domain definition
•Model execution
•Model evaluation and optimization
•Benchmarking
•Visualization and reporting
Design principles:
•
•Modularized methodology for extendibility and interoperability
•Isolation of model decisions in a central configuration system
•Facilitating machine operability for computational exploration and optimization

## Slide 8: Outline
Community Hydrological Modelling Recipes
Computational Resources for the Training Session
Setting up ECCC’s National Water Model—MESH
Introduction and Preview of CONFLUENCE

## Slide 9: Computational Resources
The idea is to expand computational performance horizontally (multiple CPUs), instead of vertically (one massive CPU)
HPC nodes are located inside rack enclosures
High Performance Computing (HPC) systems are comprised of various “nodes”
Wikipedia (accessed February 13th, 2025)
  “High-performance computing (HPC) is the use of supercomputers and computer clusters to solve advanced computation problems.”
https://top500.org/

## Slide 10: Computational Resources
Our recommendation is to connect to HPCs using either of the following methods:
Terminal
Multi-user environment
Resource efficient
Collaborative environment
Reproducibility mechanisms
Strong community support
Ease of use
Maximal flexibility
Remote Access
Steep learning curve
Full control of command sessions
Strong community support
$ ssh USERNAME@HPC_URL
MobaXTerm
PuTTY
MacOS Terminal
Notes: JupyterHub: https://jupyterhub.sharcnet.ca/

## Slide 11: Computational Resources
Science and Policy
Decisions
Subset
Regrid
Visualize
Temporal Disaggregate
HPC
Tailored
Remap
Suite of tools to facilitate hydrological modelling and data processing:
Generalizing approaches applicable to data processing applications
Using stable tools to assure robust performance on HPC platforms
Various HPCs

## Slide 12: Computational Resources
How can we launch a Jupyter session on HPCs? A few examples…
Anvil at Perdue University
Fir at Simon Fraser University
ARC at the University of Calgary

## Slide 13: Computational Resources
ARC at the University of Calgary
Since not everybody has access to an HPC, we need to separate into two groups:
Notes: Mention that even if you do have access to the HPC, but now our computational space, then still use the Cloud system.

## Slide 14: Computational Resources
HPCs typically come with various
“modules”
Different users have different requirements
Flexibility
Users may need specific versions of software or libraries
Customization
Optimization
software packages are often optimized for the underlying hardware architecture
Having commonly used software readily available, saves users time and effort
Productivity
DALL-E 3 generated image

## Slide 15
Modern scientific codes rely on icebergs of dependency libraries
71 packages
188 dependencies
LBANN: Neural Nets for HPC
MFEM: Higher-order finite elements
31 packages,
69 dependencies
r-condop: R Genome Data Analysis Tools
179 packages,
527 dependencies
Slide is obtained from Spack’s presentation titled: “Spack: Package Management for HPC.” ATPESC 2024 Software Track. Todd Gamblin.

## Slide 16
Any questions so far?

## Slide 17: Computational Resources
Notes: If you don’t know you have access to the ARC HPC, that means you are in the Cloud group.

## Slide 18: Computational Resources
ARC at the University of Calgary
Notes: We want to use the Jupyter session

## Slide 19: Computational Resources
General tips:
Understand your setup: Be resourceful—Asking too much computational resource can keep you in the queue forever
Choose the Right Kernel: Be mindful—Jupyter provides you with all sort of programming environments; make sure to choose the right (customized) programming kernel for your work.
Monitor Performance and Document: Be diligent—As you work more with the environment, you get to know the requirements of your computations. Keep track of your workflow’s performance and document your work.
DALL-E 3 generated image
DALL-E 3 generated image
Notes: JupyterHub: https://jupyterhub.sharcnet.ca/

## Slide 20: Computational Resources
Simple file browser
List of running kernels
GPU list (is your workflow for Deep Learning?)
Headers of your notebooks (just like your physical notebooks)
List of HPC modules
(explained later)
Jupyter Extensions
(disabled)
Kernel Status
List of kernels
as Notebooks
List of kernels
as consoles
Useful tools
Manu bar
Debug tools

## Slide 21: Computational Resources
List of HPC modules
(LMOD Extention)
Loaded modules
Unloaded modules
A saved list of modules
is called a “collection”
Create a collection
out of loaded modules
Restore a previously
saved collection
Using JupyterLab interface
For creating collections could be time consuming.
We will use the Terminal to build a collection later.

## Slide 22: Computational Resources
username
(usually) the node name
Current working directory
tilda means home
All instructions are available on this presentation's repository:
https://github.com/CH-Earth/community-modelling-workflow-training

## Slide 23: Computational Resources
username
Computing node name
Current working directory
tilda means home
All instructions are available on this presentation's repository:
https://github.com/CH-Earth/community-modelling-workflow-training
Getting a list of available modules
Loading
every module we need
Double checking whatever
I have loaded
Exactly similar to what
we can do in this tab
Notes: https://github.com/kasra-keshavarz/community-modelling-workflow-training

## Slide 24: Computational Resources
All instructions are available on this presentation's repository:
https://github.com/CH-Earth/community-modelling-workflow-training
Saving the modules
as a “collection”
Exactly similar to what
we can do in this tab
Notes: https://github.com/kasra-keshavarz/community-modelling-workflow-training

## Slide 25: Computational Resources
Refresh the JupyterLab session webpage, and see if you can find the collection you just saved:
Check out what module
collections you have
Restore the “scimods”
(science modules)
Wait for a few seconds
so Jupyter loads all
modules saved in
“scimods” collection
This is only a one-time process.
You can always access all the collections you saved from Jupyter’s module extension tab

## Slide 26
Any questions so far?

## Slide 27: Computational Resources
Python Programming Language
Community Hydrological Modelling Workflows: much of our workflows are offered in Python package formats
Python is Powerful: Python always can offer you a useful workflow
Reproducible Environments: Python’s Virtual Environments enables this requirement
Supported on HPCs and Commercial Cloud regardless of your Operating System: it can be used everywhere
Graham is no exception: Python is fully supported on Graham
Notes: We need to download the repository too

## Slide 28: Computational Resources
Before setting up the Python Environment, we
need to download the training session’s GitHub repository
Please note that Binder users, need to run the following command on MyBinder
Session due to a bug reported in JupyterLab:
bash --norc --noprofile
See the following webpages for ongoing discussions:
https://github.com/jupyterhub/mybinder.org-deploy/issues/3210#event-16270107011
&
https://github.com/jupyterhub/repo2docker/issues/1405

## Slide 29: Computational Resources
“clone”-ing the repository
We use this terminal session now to download the relevant GitHub repository
Notes: While this

## Slide 30: Computational Resources
Creating an empty
Virtual Environment
Activating the empty
Virtual Environment
Notes: While this

## Slide 31: Computational Resources
Installing necessary Python
Packages
Notes: While this

## Slide 32: Computational Resources
“scienv” virtual environment is now accessible through JupyterLab

## Slide 33: Computational Resources
The “scienv” (science
environment) kernel is
now recognized by
Jupyter
Refresh the JupyterLab session webpage, and see if you can find the collection you just saved:

## Slide 34: Outline
Community Hydrological Modelling Recipes
Computational Resources for the Training Session
Setting up ECCC’s National Water Model—MESH
Introduction and Preview of CONFLUENCE

## Slide 35: Setting up ECCC’s National Water Model—MESH
Command Line Interface
(CLI)
NCAR-GWF WRF CONUS I
ECMWF ERA5
ECCC RDRSv2.1
NCAR-GWF WRF CONUS II
CCRN CanRCM4-WFDEI-CaPA
https://github.com/CH-Earth/datatool.git
Steps:
1. Login to cluster of choice,
2. Make sure you have access to the designated project space and allocation,
3. Clone the remote GitHub repository,
4. Subset any spatial and temporal extents of interest for any of the available datasets
with only one line of code.
CCRN WFDEI-GEM-CaPA
.
.
.
~1 PB of data
(and growing)
AMES GDDP-CMIP6
Ouranos ESPO-G6-R2 RDRSv2.1
Ouranos CRCM5-CMPI6
DALL-E generate image
datatool
Notes: https://github.com/kasra-keshavarz/datatool

## Slide 36: Setting up ECCC’s National Water Model—MESH
ECCC Collab
ECCC Science
Ucalgary ARC
DRAC Graham
datatool
(HPC-agnostic)
https://datatool.readthedocs.io/
Hardware dependent job settings
Scheduler dependent settings
HPC-specific settings
JSON configuration files
JSON
files
… any other HPC

## Slide 37: Setting up ECCC’s National Water Model—MESH
Command Line Interface
(CLI)
MERIT-Hydro
Soil Grids V1
MODIS Land Cover
https://github.com/CH-Earth/gistool.git
Steps:
1. Login to your cluster of choice,
2. Make sure you have access to the designated project space and allocation,
3. Clone the repository,
4. Subset and/or implement zonal statistics for any spatial and temporal extents of interest
for any of the included datasets with only one line of code.
Subsetting Geo-spatial data in GeoTIFF format
Implementing Zonal Statistics for ESRI Shapefiles efficiently
Calculating Slope & Aspect [in progress]
HRUs discretization in any spatial scale [in progress]
Landsat NALCMS
Depth to bedrock
Global Soil Dataset (GSDE)
.
.
.
gistool

## Slide 38: Setting up ECCC’s National Water Model—MESH
https://github.com/ShervanGharari/EASYMORE.git
Command Line Interface (CLI)
and
Python Library

## Slide 39
Any questions so far?

## Slide 40: Setting up ECCC’s National Water Model—MESH
Configuring ECCC’s MESH with the following datasets for the Bow River at Calgary:
Meteorological Forcing Dataset | Landcover Dataset | Geospatial Fabric Dataset | Study Area
Regional Deterministic Reforecast System version 2.1 (RDRSv2.1) | North American Land Change Monitoring System 2020 (NALCMS 2020) | MERIT-Basins | Bow River at Calgary

## Slide 41: Setting up ECCC’s National Water Model—MESH
First step is to extract a geospatial fabric
for the area of interest
DALLE generated image

## Slide 42: Setting up ECCC’s National Water Model—MESH
All instructions are available on this presentation's repository:
https://github.com/CH-Earth/community-modelling-workflow-training
Bow River at Calgary
Sub-basins and river network extracted from MERIT-Basins using Hydrant v0.1.0-dev0
Calgary

## Slide 43: Setting up ECCC’s National Water Model—MESH
What information is provided through MERIT-Basins?
25 km2 drainage area threshold for channels
Corrected/refined basin/region definitions
Below 25 km2 non-channelized areas along the coast or some endorheic areas (incomplete catchments or hillslopes) excluded
~2.94 million river reaches (unit catchments)
River network:
River segment IDs (COMID)
Downstream segment IDs (NextDownID)
Slope (slope)
Length (lengthkm)
Upstream segment IDs (up1-4)
Upstream drainage area (uparea)
River geometries
MERIT-Basins webpage: https://www.reachhydro.org/home/params/merit-basins
Subbasins:
Identical subbasin IDs (COMID)
Subbasin area (unitarea)
Subbasin geometries
Non-contributing areas:
Non-contributing area IDs (FID)
Non-contributing area geometries

## Slide 44: Setting up ECCC’s National Water Model—MESH
Bow River at Calgary
Sub-basins and river network extracted from MERIT-Basins using Hydrant v0.1.0-dev0
What typical information we usually need from a hydrography dataset for vector-based hydrological modelling?
River network:
River segment ID values
Immediate downstream segment ID values
Length Depending on your routing scheme you may need:
Slope [optional]
Width [optional]
etc.
Subbasins:
Subbasin ID values
Correspondence Mapping Table between Subbasin and River Segment IDs (could be identical value)
Subbasin Area [optional]
etc.

## Slide 45: Setting up ECCC’s National Water Model—MESH
Second step is to run the model-agnostic
processes
DALLE generated image

## Slide 46: Setting up ECCC’s National Water Model—MESH
Through a tool called “agnostic orchestrator” all the relevant data needed for this setup is processed by the Graham HPC
We have previously downloaded all the relevant tools for the “agnostic” step
We use the “agnostic orchestrator” configuration file instruct the file processing hierarchy

## Slide 47: Setting up ECCC’s National Water Model—MESH
Agnostic workflow execution using its
“Orchestrator”
Editing “agnostic” configuration step

## Slide 48: Setting up ECCC’s National Water Model—MESH
Executable paths
Executable arguments and options
(empty options are ignored)
This is the only file for the “agnostic” step
Orchestrator configuration file

## Slide 49: Setting up ECCC’s National Water Model—MESH
Geospatial data zonal statistics
NetCDF Aerial Averaging
#1
#2
#4
#3
#
: Order of process
Automated and ordered job
submission to HPC
NetCDF subset
-1: no order
ordered integers: order of processes

## Slide 50
Any questions so far?

## Slide 51: Setting up ECCC’s National Water Model—MESH
Navigate using JupyterLab file browser

## Slide 52: Setting up ECCC’s National Water Model—MESH
Third and final step is to run the model-specific
processes
DALLE generated image

## Slide 53: Setting up ECCC’s National Water Model—MESH
The specific part is written into a Jupyter Notebook
(it can be written as a script or any other form that you prefer)
Meshflow is the package to build a MESH model out of all the data we processed so far
The root address of where the data is stored

## Slide 54: Setting up ECCC’s National Water Model—MESH
River network geometry file
Subbasin geometry file
Landcover fractions file(s)
Prepared forcing file(s)
List of variables to be used
Variables’ default units in the NetCDF files
Units of variables that MESH requires

## Slide 55: Setting up ECCC’s National Water Model—MESH
River Segment/Subbasin ID
Downstream river segment/subbasin ID
Landcover classes of the landcover dataset used
All the variables to be used in the “drainage database” MESH file
Units of variables to be included in the “drainage database” MESH file

## Slide 56: Setting up ECCC’s National Water Model—MESH
Units of variables in the “drainage database” file that MESH requires
Minimum values of “drainage database” MESH file
Renaming GRU dimension name in the MESH “drainage database” file to satisfy diverse versions of MESH
Renaming sub-basin dimension name in the MESH “drainage database” file if needed
The value of the outlet river segments created using “Hydrant”
(Hydrant default is -9999)
Initiate an instance of the MESHWorkflow object
And running the “model-specific” step

## Slide 57
Any questions so far?

## Slide 58: Setting up ECCC’s National Water Model—MESH
Switching to the relevant Jupyter Notebook
webpage

## Slide 59: Outline
Community Hydrological Modelling Recipes
Computational Resources for the Training Session
Setting up ECCC’s National Water Model—MESH
Introduction and Preview of CONFLUENCE

## Slide 60: Brief background: Yukon River basin study
Observations:
  53 Stream gauges
  86 Snow observation stations
  35 sub-basins with in-situ snow observations
Model: SUMMA
  Flexible framework for model comparison
  40 processes with multiple representation options
    Space of possible combinations > 107
  126 parameters to optimize for each combination
External decisions:
  Domain representation
  Forcing data
  Attribute data
  Etc.
Research Question:
How can we optimally represent hydrological processes across diverse landscapes in modern process-based hydrological models?

## Slide 61: Brief background: Yukon River basin study
Observations:
  53 Stream gauges
  86 Snow observation stations
  35 sub-basins with in-situ snow observations
Model: SUMMA
  Flexible framework for model comparison
  ~40 processes with multiple representation options
    Space of possible combinations > 107
  126 parameters to calibrate for each combination
External decisions:
  Domain representation
  Forcing data
  Attribute data
  Etc.
Research Question:
How can we optimally represent cold region hydrological processes across diverse landscapes in modern process-based hydrological models?
61

## Slide 62: CONFLUENCE: Community Optimization Nexus For Large-domain Understanding of Environmental Networks and Computational Exploration
Problem:
The inherent complexity of modern process based hydrological models poses substantial challenges to researchers and operators, particularly due to the high dimensionality of the modelling decision space
Solution:
Automation of routine task through seamless integration of existing workflows with clear separation of technical implementation and scientific decision making.
Implementation:
Single configuration file (YAML)
Central workflow orchestration script
Central workflow logging
Modular design
Extendable code base

## Slide 63: CONFLUENCE: Community Optimization Nexus For Large-domain Understanding of Environmental Networks and Computational Exploration
CONFLUENCE Workflow (Eythorsson et al., In prep.)
Problem:
The inherent complexity of modern process based hydrological models poses substantial challenges to researchers and operators, particularly due to the high dimensionality of the modelling decision space
Solution:
Automation of routine task through seamless integration of existing workflows with clear separation of technical implementation and scientific decision making.
Implementation:
Single configuration file (YAML)
Central workflow orchestration script
Central workflow logging
Modular design
Extendable code base

## Slide 64: CONFLUENCE: Community Optimization Nexus For Large-domain Understanding of Environmental Networks and Computational Exploration
Configuration examples
  Delineation
  Discretization
  Benchmarking
  Model initiation
  Model comparison

## Slide 65: INDRA: Intelligent Network for Dynamic River Analysis
New problem:
Computational resource restrictions prohibit exhaustive search of the modelling decision space using current optimization algorithms
Solution:
Reduce dimensionality of decision space by selection of a domain expertise informed subset. Leverage novel developments in LLM contextual understanding and multi-agentic AI for decision support and automation of non-essential technical implementation through configuration generation.

## Slide 66: INDRA: Intelligent Network for Dynamic River Analysis
INDRA (Intelligent Network for Dynamic River Analysis, (Eythorsson & Clark, 2025))
Implementation:
CONFLUENCE coupling with a multi agent framework orchestrated by central LLM Moderator
Moderator interacts with human operator and analyses natural language input to provide actionable decision support
Moderator can create a panel of project appropriate AI subject matter experts to deliberate on each decision
Moderator summarizes panel discussions and generates a CONFLUENCE config file with the suggested settings for the operator to consider.
If approved moderator executes CONFLUENCE.
After completed simulation Moderator generates a panel to analyze the results and suggest refinements
Repeat until results are acceptable

## Slide 67: INDRA: Intelligent Network for Dynamic River Analysis
Perceptual model generation
  Not all LLMs created equal
  Fast moving technology
Configuration rationale
  Collaborative conversation summary
Prompt parsing, e.g.:
  python INDRA.py --purpose “Please create a SUMMA model for the Congo River”
Anthropic GPT
ANVIL GPT

## Slide 68: DELTA: Deliberately Expert Liquid Topography Assistant
Next problem:
Human and economic resource restrictions bottlenecks scientific exploration and documentation.
Solution:
Individual and domain tailored AI research assistance. With appropriate access to research tools such as MAF/INDRA/CONFLUENCE along with data and computational resources to use them. Freely available and easily accessible online in all languages.

## Slide 69: DELTA: Deliberately Expert Liquid Topography Assistant
Implementation:
Online frontend
  User Interface
  Collaborative exploration
  Result exports
Backend orchestration
  Frontend API
  LLM / AI / TTS service APIs
  Misc. communication with tools
Toolbox (extendable)
  Modeling workflows (CONFLUENCE / INDRA)
  Data analysis (MAF)
  Knowledge database (SQL)
  Educational content
External data sources
Protype framework online
DELTA Frontend – User Interface (JavaScript, CSS, React)
DELTA Orchestrator / SQL database - API Layer (Python –Flask/FastAPI, PostgrSQL)
Tooling Layer (Python, Shell, R, Fortran, C++, Matlab, etc., etc.)
Educational
CUAHSI
Modelling
INDRA
CONFLUENCE
Earth Science data access
MAF
Characters
INDRA Chairperson
INDRA Expert Panel
Hydrologist teacher
DELTA
Session Management
Request Routing and Validation
Authentication & Authorization
Integration with Central LLM (Anthropic Claude)
Role-Specific Prompt Engineering & State Management
Long term memory management and logging
Knowledge base
Scientific
User data
External Data Sources (APIs, Databases, Files, etc. )
API Gateway

## Slide 70: Future Directions
Continue fusion of community assets
  Design wrappers for individual assets
  Optimize central architecture
Develop AI enhancement, e.g.:
  Validation protocols
  Evaluation philosophy
  Retrieval Augmented Generation (RAG)
  Prompt engineering
Develop interfaces
  Develop integration philosophy
  Estimate resource requirements

## Slide 71: Thank you for attending
https://ucalgary.ca/civil

## Slide 72: Backup slides

## Slide 73: Computational Resources
1 | Only for personal use | Home space 500 GB per user on ARC
2 | Only for data processing | Scratch space 15 TB per experiment
3 | NOT for personal use – only for shared resources | Project space comphyd_lab: 0.2 PB
DALL-E 3 generated image

## Slide 74: Setting up ECCC’s National Water Model—MESH
Bow River at Banff
Sub-basins and river network extracted from MERIT-Basins using Hydrant v0.1.0-dev0
How does HydrAnT help us?
Hydrant’s documentation: https://hydrantpy.readthedocs.org
Extracting subsets of hydrography datasets given a point or a boundary area,
Hydrant is data-agnostic; if the input hydrography is valid and standard, you can use Hydrant,
Common sanity checks for datasets:
  Is water going upstream?
  Is there a cycle of river segments?
  etc.
Aggregation methods to dissolve elements of hydrography datasets
Knowledge extraction:
  What is the longest branch of river segments?
  What are the upstream segment of a certain point in the river network?
  What are the downstream segments of a river segment?
  What are the Strahler order of river segment?

## Slide 75: Practice Example – Bow River at Banff
Navigate using JupyterLab file browser

## Slide 76: Setting up ECCC’s National Water Model—MESH
Use “Shift + Enter” to execute Notebook cells
Notebook cells
Double click to launch the Notebook
Tip: review keyboard shortcuts!

## Slide 77: Setting up ECCC’s National Water Model—MESH
You can view the extracted geospatial fabric in a typical GIS program, such as QGIS